## Slide 1
PROJECT DEFENCE
RouterGuardian
Predicting router failures from Huawei alarm logs — and turning each prediction into an action.
Khalil · August 2026
Notes: Ten minutes. The story: routers announce their own failures hours in advance, nobody reads it, and we built the thing that does.

## Slide 2
PART ONE
Before the project:
learning the network
Six weeks of study before a line of code — because you cannot predict a network failure without first understanding the network.
Mobile networks
2G → 5G
Routing protocols
IGP, BGP
MPLS & VPNs
labels, VRF
Data centres
spine-leaf
Huawei VRP
hands-on CLI
Notes: Thirty seconds. Frame it: the project needed domain knowledge first, and this is what that period covered.

## Slide 3
MOBILE NETWORKS
Four generations, one direction of travel
Voice stops being special
2G reserved a dedicated circuit per call. By 4G voice is just data over IMS.
Radio intelligence keeps moving
Centralised in the BSC/RNC, flattened into the eNodeB, then split again into CU/DU/RU.
Control and user planes separate
In 5G the user-plane function can sit at the edge, close to the subscriber.
Notes: Do not list the acronyms. Give the one-line direction: circuit to packet to cloud.

## Slide 4
ROUTING PROTOCOLS
How routers agree on where to send a packet
What an operator actually runs
IS-IS or OSPF inside the network for reachability, BGP at the edges for policy, and MPLS or Segment Routing underneath to steer traffic along chosen paths.
Notes: The three-way split is the whole slide: inside, between, and underneath.

## Slide 5
MPLS, SEGMENT ROUTING & VPNs
Carrying many customers over one network
Classic routing reads the destination IP at every hop. MPLS attaches a label once, and every router afterwards just follows the label — faster, and the path can be chosen in advance. Segment Routing goes further and writes the whole route into the packet, removing the need for a separate label-distribution protocol.
VRF
A virtual router inside a physical one. Two customers can both use 192.168.1.0/24 without ever seeing each other.
RD
A tag that makes each customer's overlapping address unique while it crosses the operator's core.
RT
The shipping label. It tells the receiving router which customer's table the route belongs in.
Together these are MPLS L3VPN — how one physical network carries hundreds of separate corporate networks that never see each other.
Notes: Use the postal analogy if asked: MPLS is putting a routing label on the parcel once instead of re-reading the address at every sorting centre.

## Slide 6
DATA CENTRE ARCHITECTURE
One question: how do you connect 100 racks?
Spine and leaf
You cannot cable every switch to every other — 100 switches would need ~5,000 links. A middle layer solves it in two hops.
VXLAN
Wraps an Ethernet frame inside an IP packet, so a VM can move between racks and keep its address.
BGP EVPN
Instead of flooding to find where a machine lives, every leaf announces what is behind it in advance.
This matters for the project: an operator's 4G and 5G core is no longer dedicated hardware — it is software running on servers in exactly this kind of fabric.
Notes: End on the link to the project: the network being monitored is increasingly a data centre.

## Slide 7
HANDS-ON
From theory to the command line
1
Huawei VRP
The operating system on Huawei routers and switches. Learned the view hierarchy — user, system, interface, protocol — and the habits that differ from Cisco: display instead of show, undo instead of no.
2
Configuration practice
Device setup, AAA and remote access, interface addressing, VLANs, and OSPF, built and tested in eNSP against the HCIA-Datacom syllabus.
Where it led
Studying Huawei's own documentation is what made the project possible. The alarm reference that the model is built on — every alarm's meaning, its probable causes and its repair procedure — is the same vendor documentation used to learn the platform.
1,973 alarm definitions came from there.
Also studied: HVPN — Huawei's hierarchical L3VPN, where access, aggregation and core routers each carry only the routes they need.
Notes: Bridge slide. Land the last line: the vendor documentation studied here became the dataset the model was trained on.

## Slide 8
PART TWO
The project
RouterGuardian — predicting router failures from alarm logs.
Notes: Short pause. Move on quickly.

## Slide 9
THE PROBLEM
A router tells you it is failing.
For hours. Nobody is reading.
1
Thousands of alarms a day
A medium network floods the operations centre. Almost all of it is noise.
2
Failures announce themselves
Degrading hardware raises alarms with rising frequency for hours beforehand.
3
The team reacts after the fact
By the time a Critical alarm fires, service is already gone.
The cost
When a router fails, everything downstream of it loses service.
A core router can carry 40+
devices beneath it.
Notes: Set up the gap: the information exists, it is just unread. That gap is the opportunity.

## Slide 10
WHAT WE BUILT
Read the last 24 hours. Predict the next 12. Act on it.
RouterGuardian scores every router in the network, and every prediction is routed to the action that actually fixes it.
HARDWARE FAULT
Alert the on-call team
A board, an optic, a fan. No script can fix it — a human is paged, with the alarms, the reasons and the vendor's repair procedure.
SOFTWARE FAULT
Attempt scripted remediation
A stuck process, a dropped session. The system tries the fix automatically and tells the team it is doing so.
The split matters: it is the difference between waking someone at 3am and not having to.
Notes: One sentence for the whole project. The two-way split is what makes it operational rather than academic.

## Slide 11
THE DATA
Real vendor documentation, a simulated network
1,973
Huawei alarm
definitions extracted
48,627
alarm events
generated
120
devices over
182 days
No operator log was available, so the event stream is synthetic — built from real alarm names, severities and repair procedures. Every result in this deck is measured on that data, and we are explicit about what it proves.
Notes: Be upfront about the synthetic data here, once, early. It buys credibility for everything after it.

## Slide 12
THE MODEL
Two questions, asked in order
Why two stages
Fault windows are rare — one model would drown the signal.
Each stage gets its own operating point.
It matches how the team actually decides.
26 features per window: alarm volume, type mix, severity, how fast activity is accelerating, and the router's own fault history.
Notes: Stage 2 only ever runs on what Stage 1 flagged. That is why fault type is blank for healthy routers.

## Slide 13
RESULTS
Four out of five failures caught before they happen
At the deployed threshold
80%
of real failures are predicted before they occur
The trade we chose
About half of the alerts are false. Missing an outage costs more than an engineer checking a healthy router.
Measured on a time-separated held-out split — the model is tested only on windows from later than anything it trained on.
Notes: If asked about precision: it is a deliberate recall-first operating point, and the threshold is a business decision the operator can move.

## Slide 14
DOES IT ACTUALLY WORK
The risk curve rises into the real failures
One router, four months. The model is re-scored at each point using only the alarms it had at that moment. Pale vertical lines are failures that really happened; the ringed peaks are where an alert would have fired.
Notes: This is the strongest slide. The spikes line up with the real episodes and it was not constructed to — it is a replay.

## Slide 15
EXPLAINABILITY
Every score comes with its reasons
Not a black box
Each prediction carries exact TreeSHAP contributions — how far every feature moved this router away from the fleet average.
An engineer can see why this router and not its neighbour — which is what makes the alert actionable at 3am.
Notes: Judges often ask about interpretability. This is the answer, and it is exact rather than approximate.

## Slide 16
FROM PREDICTION TO ACTION
The prediction leaves the screen
1
Automatic alert
The on-call team is emailed the moment a hardware fault is predicted — with the alarms behind it, the model's reasons, the blast radius, and Huawei's documented repair procedure.
2
Troubleshooting assistant
A link in the email opens a conversation grounded in that incident. It answers what to do first, how urgent it is and why the router was flagged — from the stored facts, never invented.
3
Root-cause comparison
Two routers side by side: location, physical environment, hardware age and topology. It says which of them plausibly explains the risk gap, and which is ruled out.
A prediction nobody sees is worth nothing. This is the half that makes it a system rather than a model.
Notes: Emphasise: the email is a work order, not a notification. It contains everything needed to act.

## Slide 17
THE APPLICATION
Built to be used, not demonstrated
[ paste a screenshot of the Fleet or Overview tab here ]
Live topology, coloured by predicted risk
Every router ranked, with blast radius
Risk replay per router over months
Alert outbox and CSV export
Notes: Keep this short — if there is a live demo, this is where it goes instead.

## Slide 18
HONEST LIMITS
What real data would change
Results would become evidence
Today the model is tested on data built alongside it. Real logs turn a coherent method into an empirical result.
Scores would drop, and that is fine
Real precursors are noisier. A model catching half of the failures still beats discovering all of them afterwards.
Impact would become real
The topology is synthesised. With a real inventory, ranking by risk times customers affected is what an operations centre actually wants.
The method and the system are real. Only the evidence is synthetic — and swapping in real logs exercises the same pipeline end to end.
Notes: Volunteer the limitation before the panel finds it. Then show you know exactly what the next step is.

## Slide 19
IN SUMMARY
From an unread alarm stream
to an actionable prediction.
1,973
real Huawei alarm
definitions
0.940
ROC-AUC,
80% recall
12h
warning before
a failure
2
remediation paths,
automatic
Thank you — questions welcome.
Notes: Close on the 12 hours. That is the number the panel should remember.